## Slide 1: Comsats University Islamabad
Final Year Project Presentation
Department of Electrical and Computer Engineering

## Slide 2: Automated Detection of White Blood Cells (Leukocytes) in Digital Microscopic Image
Supervised By: Dr. Ahsan Khawaja
Presented By:
Waleed Ahmed (FA18-BCE-065)
Muhammad Haris Siddiqui (FA18-BCE-080)
Hasnain Ahmad (FA18-BCE-068)

## Slide 3: Problem Statement
Valuable time of pathologist is wasted by the WBC counting process
Manual identification of white blood cells is a difficult and labor-intensive process
Chances for human error remains in the manual identification
Skilled pathologist are required in the manual process, but in remote areas such health professionals and infrastructure are not available

## Slide 4: Project Objectives
To review already proposed white blood cell segmentation techniques and algorithms
To develop an automated system that can segment white blood cells in the digital microscopic image from its background
To compare the performance measures (Accuracy, Specificity and Sensitivity) of our technique with previously proposed techniques
To improve performance measures by using modern image pre-processing techniques

## Slide 5: Literature Review
Type | Method | Year | Accuracy % | Specificity % | Sensitivity %
 | Mohamed and Far (2012) | 2012 | 97.9601 | 99.5129 | 87.4141
Unsupervised | Madhloom et al. | 2015 | 95.7978 | 98.9475 | 96.8925
 | Ghane N, Vard A, Talebi A, Nematollahy | 2017 | 98.4708 | 98.6014 | 93.8764
 | J. Wu, P. Zeng, Y. Zhou and C. Olivier | 2006 | 94.4325 | 97.4907 | 91.3214
 | Hegde, R. B., Prasad, K., Hebbar | 2019 | 99.4764 | 97.0856 | 94.6675
This is the research paper we Implemented
This is the research paper on which the
optimizations are based

## Slide 6: Methodology
Flow Chart

## Slide 7: Methodology
Initial Implementation
Optimized Implementation
Changing Color Domain
RGB Image
Grayscale Image
RGB Image
C component of
CMYK Image

## Slide 8: Methodology
Initial Implementation
Optimized Implementation
Contrast Enhancement
Linear Contrast Stretching
Histogram Equalization
R1
R1
Histogram Equalization
R2
2 x
Linear Contrast Stretching
Histogram Equalization
Resulted Image

## Slide 9: Methodology
Initial Implementation
Using 3x3 Filter with 3 Iterations
Optimized Implementation
Using 2x2 Filter with 7 Iterations
Minimum Filtering
Image before Filtering
Image After Filtering
Image before Filtering
Image After Filtering

## Slide 10: Methodology
Morphological Operations
Initial Implementation
Opening Operation
Optimized Implementation
Opening followed by a closing operation
Binary Image obtained after thresholding
After Morphological
Opening
After Morphological
Closing
Binary Image obtained after thresholding
After Morphological
Opening

## Slide 11: Methodology
Area Check
If the Area is greater than 5000 Pixels
Is not a White Blood Cell
Is a White Blood Cell
No
Yes
Image Before Area Check
Image After Area Check

## Slide 12: Evaluation Criteria
True Positive (TP): Correctly detected foreground pixels.
True Negative (TN): Correctly detected background pixels.
False Negative (FN): Not Correctly detected background pixels.
False Positive (FP): Not Correctly detected foreground pixels.
Original Image
Ground Truth Image
Resultant Image

## Slide 13: Evaluation Criteria
Performance Measures
The ratio of truly detected pixels to the total
number of pixels in the image
Accuracy :
Accuracy
Specificity :
The ratio of truly detected background pixels
to the total background pixels
Sensitivity :
The ratio of truly detected foreground pixels
to the total foreground pixels
Resultant Image
Ground Truth Image

## Slide 14: Results & Comparison
Results of Initial Implementation
Average Accuracy | Average Sensitivity | Average Specificity
0.979601134 | 0.874141382 | 0.995129388
Average Performance Measures
Performance measures for all 100 images in Graphical Representation

## Slide 15: Results & Comparison
RGB Color Domain to CMYK Color Domain Implementation Results
Parameters | RGB Color Domain | CMYK Color Domain
Average Accuracy | 0.979601134 | 0.976753175
Average Specificity | 0.995129388 | 0.979220785
Average Sensitivity | 0.874141382 | 0.949528978
Average Performance Measures
Performance measures for all 100 images in Graphical Representation

## Slide 16: Results & Comparison
3x3 Min Filter to 2x2 Min Filter Implementation Results
Parameters | 3x3 Min Filter | 2x2 Min Filter
Average Accuracy | 0.976753175 | 0.975609864
Average Specificity | 0.979220785 | 0.978573548
Average Sensitivity | 0.874141382 | 0.949528978
Average Performance Measures
Performance measures for all 100 images in Graphical Representation

## Slide 17: Results & Comparison
Morphological Closing & Morphological Opening Implementation Results
Parameters | Morphological Opening | Morphological Opening & Closing
Average Accuracy | 0.975609864 | 0.971635147
Average Specificity | 0.978573548 | 0.972264606
Average Sensitivity | 0.94317967 | 0.970664008
Performance measures for all 100 images in Graphical Representation
Average Performance Measures

## Slide 18: Conclusions
Reviewed already proposed white blood cell segmentation techniques and algorithms
Developed an automated system that can segment white blood cells in the digital microscopic image from its background
Modern Supervised Learning-based Algorithms can be used in near future for more precise segmentation
The proposed scheme is applied on 100 WBC images and compared with manual segmentation result by three performance measures (Accuracy, Specificity and Sensitivity).